## Slide 1: DCAP: Data Link Switching Client Access Protocol
Santanu Mondal
24MTNISPY0004
Pondicherry University

## Slide 2: Protocol Description
DCAP is an application layer protocol between workstations and routers to transport SNA/NetBIOS traffic over TCP sessions.
It is a protocol to facilitate communication between client systems and the Data Link Switching (DLSw) network.
Primarily used in enterprise networking for SNA (Systems Network Architecture) and NetBIOS traffic over TCP/IP networks.

## Slide 3: Purpose of DCAP
Allows non-DLSw devices to communicate with DLSw networks.
Provides a standard method for client devices to access SNA and NetBIOS services.
Enhances interoperability between legacy systems and modern IP-based networks.

## Slide 4: How DCAP Work
In a DLSw (Data Link Switching) network, a workstation must have a MAC address to communicate with an FEP (Front-End Processor) attached to a LAN.
When a workstation connects via PPP (Point-to-Point Protocol) (e.g., through a modem), it may only have an IP address and no predefined MAC address. Without a MAC address, DLSw cannot function properly.
To solve this, administrators must manually assign a virtual MAC address to each workstation and each MAC address must be unique.
DCAP (Data Link Switching Client Access Protocol) introduces the Dynamic Address Resolution protocol to automate this process instead of manual assignment.

## Slide 5: DCAP Architecture
Consists of a DCAP client and a DLSw-enabled router or server.
The DCAP client communicates with the DLSw router, which then connects to the SNA environment.
Uses TCP/IP as the transport mechanism.
Ensures seamless transmission of legacy networking traffic over modern infrastructures.

## Slide 6: Protocol Structure
Protocol ID - The Protocol ID is set to 1000.
Version number - The Version number is set to 0001.
Message type - The message type is the DCAP message type.
Packet length - The total packet length is the length of the packet including the DCAP header, DCAP data and user data. The minimum size of the packet is 4, which is the length of the header.

## Slide 7: Reference
DCAP is defined by IETF in RFC 2114.

## Slide 8: Thank You